## Slide 1
IEEE OJCOMS • SPECIAL ISSUE: DELAY-TOLERANT NETWORKING FOR 6G
Peak Age of Information over Scheduled,
Energy-Constrained Multi-Segment DTNs
with Bundle Replication
When is a bundle copy worth its energy? A freshness theory for LEO + UAV + terrestrial contact plans.
Author name • Affiliation
Manuscript for IEEE OJCOMS — submission Aug 2026
Notes: Talk in one line: freshness (peak age of information) over DTN contact plans, where links are scheduled and intermittent, and every extra bundle copy costs harvested energy. We derive when a copy is worth its energy. Validated in Monte-Carlo and in a real Bundle Protocol / CGR simulator.

## Slide 2
THE SETTING
Scheduled, intermittent connectivity is the 6G frontier
Ground
sensor
source
UAV
mule
semi-periodic patrol
LEO
relay
periodic passes
Ground
gateway
monitor
terrestrial: renewal ON/OFF
UAV: jittered period
LEO: deterministic P, W
Links are scheduled, not lossy
A ground station sees a LEO satellite for a window W once per period P. Between passes the link is OFF by schedule — bundles age in a buffer, not in a queue.
Freshness is the metric
Telemetry, disaster response, IoT monitoring care about Age of Information and its peak (PAoI) — not throughput or delivery ratio.
Copies cost energy
DTN replication hedges uncertain contacts, but on harvesting relays every copy drains the battery that future contacts need.
PAoI over scheduled, energy-constrained multi-segment DTNs
2
Notes: Set the scene: 6G integrates non-terrestrial segments. The canonical chain: ground sensor to UAV mule to LEO relay to gateway. Three points: connectivity is scheduled (bundle ages in buffer until next pass, a residual-wait law, not queueing); the metric is freshness; and replication couples to energy on harvesting platforms.

## Slide 3
POSITIONING
Three literatures that don’t meet
AoI over erasure links
Chiariotti et al., HARQ / satellite AoI
Always-on server, random packet erasure. No scheduled OFF periods — no residual-wait law.
Tandem-queue AoI
Sinha et al., Senthilkumar et al.
Persistent or memorylessly failing servers. A contact plan is deterministic-periodic — a different law.
Contact-plan routing
CGR / RUCoP / CGR-UCoP
Optimizes delivery ratio under uncertain contacts. No freshness objective, no energy budget.
The gap: no prior work couples scheduled store–carry–forward gating + multi-copy replication + an energy constraint with a freshness objective.
Closest late-breaking work — Badia et al. (Globecom-W ’25): copy diversity lowers AoI under random intermittency, energy-agnostic. We cover the complementary regime: deterministic contact plans, finite-battery copy-degree control, CGR realization.
PAoI over scheduled, energy-constrained multi-segment DTNs
3
Notes: Reviewers here are DTN insiders (CGR lineage). Position early: erasure-channel AoI assumes always-on servers; tandem-queue AoI assumes persistent or memoryless-failing service; the space-DTN community optimizes delivery ratio, not freshness, and never models energy. We extend RUCoP/CGR rather than compete. Mention Badia Globecom-W 2025 as closest recent work: random availability, no energy; ours is deterministic scheduling + energy-coupled copy degree.

## Slide 4
SYSTEM MODEL
Duty-cycled segments, buffered aging, an energy gate
ON
OFF
W
G = P − W
period P (duty cycle δ = W/P)
arrival at phase U → residual wait R (ages in buffer)
Rₛ
residual wait until next window at segment s
Dₛ = Rₛ + Tₛ
per-segment increment (wait + service/propagation)
Y = Σₛ Dₛ
end-to-end latency; k copies → Yₘᵢₙ = minₖ Y⁽ᵏ⁾
PAoI = E[Z] + E[Yₘᵢₙ]
per-outage peak age (worst staleness per silent gap)
⚡
Energy gate. Each relay has battery bₛ, harvest rate λₑ, per-copy cost e. A contact is usable only if the battery covers the copy: Iₛᵉᶠᶠ = Iₛ · 𝟙{bₛ ≥ e}. Scarcity thins contacts; replication drains the battery faster — the tension this paper resolves.
PAoI over scheduled, energy-constrained multi-segment DTNs
4
Notes: The model: each segment is a server that is ON only during scheduled windows. A bundle generated mid-gap waits a residual R before service T. Latencies add along the chain; replication takes the min over k copies. We report per-outage PAoI = E[Z] + E[Ymin] (worst-case staleness per silent gap; conservative vs textbook per-reset PAoI). Energy gates contacts: usable only when the battery covers a copy.

## Slide 5
RESULT 1
The LEO residual-wait anchor — closed form
A stationary arrival meets the schedule at uniform phase:
P(R = 0) = δ fᵣ(r) = 1/P on (0, G]
E[R] = (P−W)² / 2P = (P/2)(1−δ)²
mean AoI = Tₛ + (P/2)(1−δ)²
peak AoI = Tₛ + P(1−δ)
Validated: KS distance 0.002; log–log slopes 1.98 / 1.00.
Chart: duty cycle δ
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
mean AoI − Tₛ (quadratic) | 0.405 | 0.32 | 0.245 | 0.18 | 0.125 | 0.08 | 0.045 | 0.02
peak AoI − Tₛ (linear) | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2
Design consequence: sparse contacts hurt the mean quadratically but the peak only linearly — mean-optimal and peak-optimal contact provisioning differ.
PAoI over scheduled, energy-constrained multi-segment DTNs
5
Notes: Result 1 is the anchor everything else builds on. Uniform arrival phase gives a mixed residual law: atom at zero (arrive in-window) plus uniform slab over the gap. Mean age is quadratic in (1-delta), peak is linear - so provisioning for mean vs peak freshness leads to different constellations. Validated to KS 0.002; fitted slopes 1.98 and 1.00.

## Slide 6
ONE MODEL, THREE SEGMENT TYPES
Renewal generalization & the AoI/PAoI inversion
Alternating renewal: ON duration U, OFF gap V;
cycle C = U + V
E[R] = E[V²] / 2E[C]
E[PAoI] = Tₛ + E[V]
LEO = deterministic V • UAV = low-jitter V • CTMC = exponential V • terrestrial = high-variance V
Exact inversion condition CV²(V) > 1 + 2E[U]/E[V]
→ peak age falls below average age (≈ CV 1.11 here)
Chart: CV of contact gap V
| 0.0 | 0.3 | 0.5 | 1.0 | 1.5 | 2.0
mean AoI | 0.41 | 0.446 | 0.511 | 0.815 | 1.322 | 2.03
mean PAoI | 0.905 | 0.905 | 0.904 | 0.904 | 0.904 | 0.903
simulation, 12 seeds — PAoI is variance-blind; AoI is not. They cross at the predicted threshold.
PAoI over scheduled, energy-constrained multi-segment DTNs
6
Notes: One alternating-renewal model covers all three segment types; LEO is the deterministic special case, the unreliable-server CTMC literature is the exponential point on our CV axis. Key structural finding: mean PAoI depends only on E[V], mean AoI grows with gap variance - so above an exact CV threshold, peak age sits BELOW average age. A single freshness number misleads across heterogeneous segments. Chart is real simulation data (E12).

## Slide 7
RESULT 2
Phase mixing composes latencies — and prices a copy
Phase-mixing lemma (Weyl)
If segment periods are incommensurate (or upstream dispersion exceeds Pₛ), arrival phases become uniform & independent ⇒ increments Dₛ are independent and end-to-end latency is their convolution.
Failure mode: a UAV synchronized to one specific LEO pass locks the phases — the correction term revives. Confirmed in dtnsim: end-to-end variance additivity holds under incommensurate periods and collapses under commensurate (locked) ones.
Two-copy PAoI theorem
E[Yₘᵢₙ] = E[Y] − ½ E|Y⁽¹⁾ − Y⁽²⁾|
The freshness bought by a second copy = half the mean absolute dispersion of path latencies (a Gini-type index).
⅔(1−δ)
two-copy residual ratio
E[Rₘᵢₙ]/E[R] — a 33% cut
at sparse contacts
0
gain for same-bottleneck
copies — replication pays only
on independent contacts
PAoI over scheduled, energy-constrained multi-segment DTNs
7
Notes: Composition needs care: a bundle's arrival phase at segment s is displaced by upstream delays. The phase-mixing lemma (Weyl equidistribution) gives the exact condition for independence: incommensurate periods or large upstream dispersion. Then the two-copy theorem: the value of a second copy equals half the Gini dispersion of path latency - replication pays in proportion to latency spread, and pays zero on same-bottleneck copies. Failure mode validated in the real CGR stack.

## Slide 8
RESULT 3
The energy–replication threshold
Mean-PAoI objective in copies k :
A(k) = P(1−pₑ)/pₑ + P(1−δ)ᵏ⁺¹/(k+1)
starvation (energy-forced skips) vs order-statistic gain
η = λₑP/e (copies harvested per contact period)
Unimodal ⇒ optimum brackets η
k* = min( Kₘₐₓ , ⌊η⌋ or ⌈η⌉ )
⌊η⌋ = conservative no-starvation rule; take ⌈η⌉ only when the extra copy repays its skips. Monotone in η, saturates at Kₘₐₓ.
Chart: replication degree k
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
η = 3 | 1.41 | 1.248 | 1.178 | 1.456 | 1.759 | 2.073 | 2.392 | 2.719 | 3.051
η = 5 | 1.41 | 1.248 | 1.169 | 1.123 | 1.102 | 1.273 | 1.458 | 1.648 | 1.849
simulated PAoI is unimodal with minimum at k = η — over-replication starves future windows.
PAoI over scheduled, energy-constrained multi-segment DTNs
8
Notes: The core result. Objective: starvation term (energy-forced skipped windows) plus order-statistic gain. Unimodal in k, minimizer is one of the two integers bracketing eta = copies harvested per period. Floor = conservative no-starvation DTN rule; ceiling wins only when a skipped window is worth the extra copy - that distinction is itself a contribution. Chart is real Tier-1 data: minimum sits exactly at k = eta.

## Slide 9
RESULT 3 — VALIDATION
The staircase, and the ceiling branch caught in the act
Chart: energy adequacy η
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
closed form min(Kₘₐₓ, ⌊η⌋) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 8
simulated k* | 1 | 2 | 3 | 4 | 6 | 8 | 8
k*(η) non-decreasing, saturates at Kₘₐₓ = 8 (Theorem 3)
The ceiling branch (E14)
Fine η-sweep across [3, 4], δ = 0.1, 16 seeds:
η | 3.1 – 3.8 | 3.9
simulated optimum | k = 3 = ⌊η⌋ | k = 4 = ⌈η⌉
analytic branch | floor | ceiling
Flip lands exactly at the analytic crossover η★ = 3.824 — 9/9 points match. Occasional energy-forced skips are worth the extra copy near the top of the interval.
PAoI over scheduled, energy-constrained multi-segment DTNs
9
Notes: Two validations of the threshold. Left: k* tracks eta one-for-one then saturates at Kmax - the staircase, real Tier-1 data. Right: E14 pins the subtle branch - between integers, the simulated optimum stays at floor(eta) through 3.8 and flips to ceiling at 3.9, bracketing the analytic crossover 3.824. 9/9 match. The floor-vs-ceiling distinction survived adversarial review.

## Slide 10
HARDENING
An exact battery-queue throttle, not a fluid guess
Work conservation (distribution-free)
k · pₑ(k) = η − L
L ≥ 0 = harvest lost to the battery cap. Only the mean η enters; the fluid rule pₑ = min(1, η/k) is exactly the infinite-battery limit. Holds to 10⁻⁵ in simulation, Poisson and deterministic harvest alike.
Finite battery ⇒ downward pressure on k∗, not a hard ceiling: the overflow loss L(B,k) varies with k, so the pₑ bound doesn’t order the objectives — a ceiling winner keeps winning for large enough B.
Chart: battery capacity B (copies)
| B = 4 | B = 5 | B = 6 | B = 64
η = 4 | 2 | 3 | 3 | 4
shrinking the battery pushes k* down (at η = 6 it falls 6 → 4 by B = 6) — quantified, not assumed.
PAoI over scheduled, energy-constrained multi-segment DTNs
10
Notes: The fluid throttle is replaced by the stationary law of a finite energy queue. Work conservation gives k*pe = eta - L, distribution-free - only the mean harvest matters at this order. Honesty slide: finite battery presses k* down empirically (bars, real data), but it is NOT a universal ceiling at floor(eta) - the overflow loss depends on k, so objectives are not ordered pointwise. This precision came out of adversarial review.

## Slide 11
FROM THEOREM TO KNOB
An O(1) two-candidate policy on top of CGR
The rule
kₚₒₗ = argmin over { ⌊η⌋, ⌈η⌉ } of A(k), clipped to [1, Kₘₐₓ]
Two objective evaluations — O(1), local, no sweep. Driven by the slow mean energy-adequacy η (a set-point, not a per-window controller). CGR picks the routes; the policy picks how many.
Prediction-error robustness: as contact predictions degrade (α → 0.4), the optimum stays at ⌊η⌋ (+19% PAoI); the “reserve energy” heuristic under-replicates (+50%). Replication is the right hedge.
Chart: energy adequacy η
| 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 5 | 6 | 8
k=1 | 1.41 | 1.41 | 1.41 | 1.41 | 1.41 | 1.41 | 1.41 | 1.41 | 1.411
k=2 | 1.58 | 1.256 | 1.248 | 1.248 | 1.248 | 1.248 | 1.248 | 1.248 | 1.248
k=3 | 2.165 | 1.668 | 1.368 | 1.177 | 1.169 | 1.169 | 1.169 | 1.169 | 1.169
k=4 | 2.787 | 2.122 | 1.723 | 1.455 | 1.265 | 1.131 | 1.123 | 1.123 | 1.123
adaptive policy | 1.41 | 1.256 | 1.248 | 1.177 | 1.169 | 1.131 | 1.123 | 1.123 | 1.123
the policy (orange) rides the lower envelope of every fixed degree — matched the exhaustive optimum at all η.
PAoI over scheduled, energy-constrained multi-segment DTNs
11
Notes: The theorem becomes a deployable knob: evaluate the objective at floor(eta) and ceil(eta) only - O(1) - and clip to Kmax. It layers on CGR: CGR answers WHICH routes, we answer HOW MANY copies. Real data: the adaptive policy rides the lower envelope of all fixed degrees and matched the exhaustive optimum at every sampled energy level. Bonus: robust to contact-prediction error - keep replicating, don't reserve energy.

## Slide 12
BEYOND THE MEAN
Deadline tails collapse; RUCoP composes, not competes
Chart: freshness deadline (units of P)
| 1.0 | 1.1 | 1.25 | 1.5 | 1.75 | 2.0
k = 1 | 1 | 0.804 | 0.654 | 0.405 | 0.155 | 0
k = 2 | 1 | 0.648 | 0.429 | 0.165 | 0.024 | 0
k = 4 | 1 | 0.42 | 0.184 | 0.027 | 0.0005 | 0
15× fewer 1.5P-deadline violations at k = 4; p99 drops 1.90P → 1.59P.
vs. a RUCoP-style MDP core
Holder-set backward induction (delivery-optimal, energy-blind) on an illustrative uncertain diamond. The delivery-vs-copies frontier is concave — copies past the knee buy little.
94.7%
of the MDP’s delivery
at our k∗ = 2
40%
of its energy
spend
Complementary: the MDP picks which routes, our threshold picks how many copies — the natural energy-aware extension of CGR-UCoP.
PAoI over scheduled, energy-constrained multi-segment DTNs
12
Notes: Two decision-maker views. Left: mission-critical traffic cares about the tail - replication pulls the deadline-violation CCDF in sharply, 15x fewer violations of a 1.5P deadline at k=4. Right: against a RUCoP-style MDP core (honest label: decision core on an illustrative instance, not benchmark-scale) - the frontier is concave, so our energy-derived degree gets ~95% of delivery for 40% of energy. The two compose: their routes, our copy count.

## Slide 13
VALIDATION — THREE TIERS
Analysis → Monte-Carlo → real Bundle Protocol/CGR
Chart: energy adequacy η
| 0.6 | 1.0 | 1.5 | 2.0 | 3.0 | 6.0
single-copy CGR | 50972 | 50536 | 49533 | 48914 | 46475 | 40189
2-copy CGR router | 7989 | 7809 | 7650 | 7574 | 7166 | 6844
dtnsim (real BP/CGR stack), 10 seeds, 95% CIs — two copies cut PAoI ~6× by hedging relay faults.
0.0%
delay error vs closed form
(2453.9 s vs 2453.9 s, full
mixed residual histogram)
0.06%
error on a real Iridium-NEXT
TLE contact plan
(101 passes, Skyfield)
1.1%
additive-residual error on the
3-hop heterogeneous chain
(sensor→UAV→LEO→gateway)
14 / 14
experiments pass
(E1–E14, incl. the η★ = 3.82
ceiling flip)
PAoI over scheduled, energy-constrained multi-segment DTNs
13
Notes: Every claim is triple-validated: closed form, model-exact Monte-Carlo (Tier 1, E1-E14 all pass), and dtnsim - a real Bundle Protocol / CGR simulator from the RUCoP lineage, extended with our energy module and a CGR-native k-copy router. Highlights: exact delay match on the synthetic plan; 0.06% on a real Iridium TLE contact plan; residual additivity on the full heterogeneous chain to 1.1%; and the 6x PAoI cut from 2-copy CGR routing under relay faults. Scenario files are public.

## Slide 14
VALIDATION — GROUND TRUTH
Real ephemeris and flight software close the loop
Chart: E[Rmin,2] / E[R1] (lower = fresher)
| anti-phased pair (ρ = −0.51) | independent ideal ⅔(1−δ) | near-indep. pair (ρ = +0.07) | phase-locked pair (ρ = +0.88)
two-copy gain | 0.41 | 0.606 | 0.635 | 0.952
44 real Iridium-NEXT pairs over Svalbard: the gain is set by pass-phase alignment — plannable from the contact plan → phase-aware copy placement.
ION 4.1.4 — reference BP flight software
974/974
bundles delivered
lossless, 2 h run
24.34 s
residual, exact per
bundle (law: 24.30 s)
2.5 ± 0.5 s
dispatch lag = the
model's Tₛ, measured
delay = R + Tₛ decomposition validated in flight code; Tₛ ≈ 0.04% at operational periods.
Bursty harvest (E15)
k* = ⌊η⌋ unchanged up to harvest dwell ≈ 10 periods; work conservation ≤ 3×10⁻⁴ under all correlation (distribution-free). Correlation moves the tail (p99 +72%), not the threshold; boundary at dwell ≈ 50.
PAoI over scheduled, energy-constrained multi-segment DTNs
14
Notes: New ground-truth tier. Left: 44 real Iridium pairs - the two-copy gain runs 0.41 to 0.95 purely on pass-phase alignment; anti-phased beats even the independent ideal, phase-locked makes replication worthless. Contact plans are known, so this is computable at planning time: phase-aware copy placement, now a numbered contribution. Right: ION flight software - 974/974 lossless, the residual law exact per bundle, and the 2.5 s dispatch lag is literally the model's T_s measured in flight code. Below: bursty harvest keeps the threshold, inflates only the tail.

## Slide 15
TAKEAWAYS
Freshness has a price in copies — now we know it
A residual-wait law, not a queueing delay
One alternating-renewal model covers LEO / UAV / terrestrial; mean quadratic, peak linear — and peak can drop below mean past an exact CV threshold.
Replication is priced by dispersion
A second copy buys ½ E|Y⁽¹⁾−Y⁽²⁾| of freshness — phase mixing tells you exactly when latencies compose.
k∗ tracks the energy budget
Launch ⌊η⌋ copies — or ⌈η⌉ when a skip is worth it — capped at Kₘₐₓ. An O(1) rule that rides the optimum on top of CGR.
Validated where DTN insiders live
Model-exact MC + real BP/CGR stack + ION flight software + real Iridium ephemeris — where phase-aware copy placement emerges as a plannable design rule.
Ongoing: regime-aware adaptation under extreme harvest persistence • RUCoP’s route set under the degree cap • tail-constrained policy
PAoI over scheduled, energy-constrained multi-segment DTNs
15
Notes: Close on the four takeaways: (1) scheduled gating gives a residual-wait law - one renewal model, all segments, with the AoI/PAoI inversion; (2) replication is priced by latency dispersion via the Gini identity; (3) the optimal copy count tracks the energy budget - floor or ceiling of eta, an O(1) policy over CGR; (4) validated down to a real BP/CGR stack and real Iridium ephemeris. Ongoing: correlated harvests, composing with RUCoP routes, tail constraints. Thank you.